## Slide 1: The Queen’s College IT Open Morning
Microsoft Network Policy Server + VLANs/ACLs

## Slide 2: What does it do?
Network Policy Server
  Authenticates devices based on
    802.1x Credentials
      Username/Password
      Certificate
    MAC Address
  Places the client in the correct VLAN + send other RADIUS Attributes

## Slide 3: Alternatives…
Bradford Network Sentry
Aruba Clear Pass
PacketFence

## Slide 4: Network Switch Config
radius-server host 172.16.0.2 key <key!!>
radius-server dead-time 1
radius-server timeout 3
radius-server retransmit 2
aaa authentication login privilege-mode
aaa authentication ssh login radius local
aaa authentication ssh enable radius local
aaa port-access mac-based addr-format no-delimiter
aaa port-access gvrp-vlans
aaa authentication port-access eap-radius
aaa port-access authenticator 1-8
aaa port-access authenticator 1-8 quiet-period 30
aaa port-access authenticator 1-8 tx-period 2
aaa port-access authenticator 1-8 supplicant-timeout 2
aaa port-access authenticator 1-8 server-timeout 10
aaa port-access authenticator 1-8 max-requests 3
aaa port-access authenticator 1-8 reauth-period 600
aaa port-access authenticator 1-8 auth-vid 1
aaa port-access authenticator 1-8 client-limit 3
aaa port-access authenticator active
aaa port-access mac-based 1-8
aaa port-access mac-based 1-8 logoff-period 862400
aaa port-access mac-based 1-8 quiet-period 30
aaa port-access mac-based 1-8 server-timeout 10
aaa port-access mac-based 1-8 reauth-period 600
aaa port-access mac-based 1-8 unauth-vid 97
aaa port-access mac-based 1-8 addr-limit 3
aaa port-access 1-8 controlled-direction in

## Slide 5
Notes: Install AD CA
Configure computer Cert

## Slide 6
Notes: Configure computer cert
Enable computer cert

## Slide 7
Notes: Enable computer cert

## Slide 24: ACLS Slide

## Slide 25: Further Reading
Lynda.com https://www.lynda.com/Windows-Server-tutorials/Overview-Network-Policy-Server-NPS/459490/505660-4.html